## Slide 1: Pinball: A Cryogenic Predecoder for Quantum Error Correction Decoding Under Circuit-Level Noise
Alexander Knapen
Coauthors: Guanchen Tao, Jacob Mack, Tomas Bruno, Mehdi Saligane, Dennis Sylvester, Qirui Zhang, Gokul Subramanian Ravi
This material is based upon work supported by the U.S. Department of Energy, Office of Science, Office of Advanced Scientific Computing Research, Accelerated Research in Quantum Computing under Award Number DE-SC0025633. This research used resources of the National Energy Research Scientific Computing Center, a DOE Office of Science User Facility supported by the Office of Science of the U.S. Department of Energy under Contract No. DE-AC02-05CH11231 using NERSC award ASCR-ERCAP0033197.

## Slide 2
Background: Surface Code Decoding + Cryogenic Predecoding
Pinball Predecoding Algorithm
Hardware Implementation
Performance Results
Overview

## Slide 3
Surface Code Decoding

## Slide 4: Quantum Error Correction
1) Data Qubits: store computational state being computed on
2) X Ancilla Qubits: detect parity of Z errors on neighboring data qubits
3) Z Ancilla Qubits: detect parity of X errors on neighboring data qubits
Surface Code
Redundantly group multiple, error prone physical qubits into a single, robust logical qubit
d = 5

## Slide 5: Quantum Error Correction
1) Data Qubits: store computational state being computed on
2) X Ancilla Qubits: detect parity of Z errors on neighboring data qubits
3) Z Ancilla Qubits: detect parity of X errors on neighboring data qubits
Surface Code
Redundantly group multiple, error prone physical qubits into a single, robust logical qubit
d = 5
Syndrome ≡ binary vector of ancilla measurement outcomes (1 = “active”, 0 = “inactive”)

## Slide 6: Surface Code Decoding
Decoding Graph Representation
  Vertices ≡ syndromes
  Edges ≡ errors flipping syndromes at their endpoint(s)
Classical Decoding Algorithm: find paths that connect active syndromes

## Slide 7: Surface Code Decoding
Noise model changes the complexity of the decoding graph
  Code Capacity: each data qubit randomly flips with some probability
  Phenomenological: accounts for imperfect measurements
  Circuit-Level: accounts for imperfect gates in syndrome measurement circuits
1
2
3
Space-like Errors
Space-like + Time-like Errors
Space-like +
Time-like +
Spacetime-like Errors

## Slide 8
Cryogenic Predecoding

## Slide 9: System-Level Decoding Challenges
1) Syndrome Data Volume
2) Decoding Complexity
3) Strict Real-Time Constraints

## Slide 10: System-Level Decoding Challenges
1) Syndrome Data Volume
2) Decoding Complexity
3) Strict Real-Time Constraints
> 90% of error chains are short (length ≤ 1)
Use lightweight, locally accurate logic to:
1) Decode common length-1 chains at cryo
2) Detect rare, longer chains and offload to RT
State-of-the-art: Clique
Cryogenic Predecoding

## Slide 11: Clique Limitations
Tailored to phenomenological noise

## Slide 12: Clique Limitations
Tailored to phenomenological noise
⇒ Limited system-level performance benefits in real-world
quantum systems
Logical Error Rate

## Slide 13: Clique Limitations
Tailored to phenomenological noise
⇒ Limited system-level performance benefits in real-world
SFQ Implementation
⇒ Relative lack of maturity precludes design evaluation + optimization

## Slide 14
Pinball Predecoding Algorithm

## Slide 15: Pinball Predecoder
Predecoding Primitive: for every pair of neighboring syndromes in the decoding graph, apply a correction on
the edge between them if they’re both active

## Slide 16: Pinball Predecoder
How do we know which data qubit(s) to correct for each edge?
Need to Cover:
Space-like Edges
Time-like Edges
Spacetime-like Edges
Predecoding Primitive: for every pair of neighboring syndromes in the decoding graph, apply a correction on
the edge between them if they’re both active

## Slide 17: Deriving Hook-like Edges

## Slide 18: Deriving Hook-like Edges

## Slide 19: Deriving Hook-like Edges
Correct the two data qubits along the chain between the pair of active syndromes in the surface code lattice

## Slide 20: Deriving Hook-like Edges

## Slide 21: Multiple Active Neighbors
Race condition: corrections are inconsistent with observed syndromes

## Slide 22: Multiple Active Neighbors
Solution:
  Enforce ordering between conflicting predecoding primitives
  Clear active syndromes when assigning corrections

## Slide 23
Hardware Implementation

## Slide 24: Predecoding Primitive
Functionality
If both syndromes in a pair are active, assign a correction to their edge
Clear the syndrome pair after assigning a correction

## Slide 25: Pinball Pipeline
Functionality
Break race conditions by enforcing an ordering between conflicting predecoding primitives

## Slide 26
Evaluation & Results

## Slide 27: L1 Accuracy
L1 Accuracy
(%)
Percentage of syndromes decoded
correctly by the predecoder
⇒ Proxy for logical error rate
At and
Pinball’s Accuracy: 100%
Clique’s Accuracy: 62.31%

## Slide 28: Logical Error Rate
How well does Pinball tradeoff coverage
and accuracy compared to Clique?
At and
Pinball’s Improvement:
Pinball is the first cryogenic predecoder to enable exponential reduction in logical error rates under realistic noise
Logical Error
Rate

## Slide 29: Logical Error Rate
How detrimental is it to introduce a
first-level heuristic decoding step?
Pinball maintains the required QEC performance for real quantum computing systems
Logical Error
Rate

## Slide 30: L1 Coverage
Percentage of syndromes handled cryogenically
by the predecoder
⇒ Proxy for syndrome bandwidth reduction
At and
Pinball’s Coverage: 98.16%
Clique’s Coverage: 1.43%
L1 Coverage
(%)

## Slide 31: Bandwidth Savings
Bandwidth
Savings
Near-Term (p = 10-3)
Prominent bandwidth savings at intermediate code distances ()
Long-Term (p = 10-4)
Orders of magnitude bandwidth savings over all code distances

## Slide 32: Energy Savings
Total Energy = Syndrome Transmission Energy + Cryogenic Hardware Energy
Pinball ↓ ↑
Near-Term (p = 10-3)
Pinball: max 15.06x savings
Long-Term (p = 10-4)
Pinball: max 39.06x savings
Energy
Savings
Pinball can support up to 37,500 logical qubits at and 2,777 logical qubits at .

## Slide 33: Key Takeaways
QEC circuit- and application-level analysis reveals critical design optimizations that circumvent key system bottlenecks
Pinball decreases logical error rate and syndrome bandwidth by several orders of magnitude relative to prior SOTA
  ⇒ First demonstrated cryogenic predecoder suitable to realistic noise
Application-hardware codesign enables Pinball to achieve energy savings for any target physical error rate or code distance
  ⇒ Enables scalability to large numbers of logical qubits within cryogenic operating constraints
Scan to read the paper!

## Slide 34: Thank You For Listening!